Meataxe64 V.2 Software Structure
R. A. Parker. 29.June.2016.

1. Introduction

Meataxe version 1 is more-or-less completed. My rush to get something out that is capable of doing multiply, nullspace and split has probably not produced the work-horse of the future, so I propose to leave it quietly behind and continue with sensible development.

The design now has a rather large number of modules – it seems that producing a system of this scale requires a fair number of layers, and this document is an overall description of the software structure as it is eventually intended to be. Much of it is in place already, but there is still quite a bit to do.

1. Bottom-up summary.

field.c is the routine way of handling field elements and vectors. It is mainly written to be of the best performance that can be achieved with the element+vector interface, and is normally used unless the operations are of performance-critical importance. It already works over all fields up to (but not including) 264, although there are some remaining performance issues for the largest fields. The vectors are stored in Dfmt, which for fields of order 2 (respectively 3,4,5) packs 8 (respectively 5,4,3) elements into a byte, for fields of order {7,8,9,11,13,16} packs two to a byte, and for fields of order 17-256 (respectively 257-65536, 65537-232, 232+1 – 264-1) uses 1 (respectively 2, 4, 8) bytes for each entry. The Conway polynomials are used throughout. The main performance pressure is on DSMad (multiply a vector/matrix by a scalar and add to another one).
pcrit.s is the module that does the lowest-level assembler code for the HPMI. There are two main versions – NEH designed for pretty-much any 64-bit x86 using SSE (128-bit vector registers) and HAS designed to use AVX-2 as first appeared with the Haswell chips from Intel. It currently can handle characteristic 2 and 3.
hpmi.c does those parts of the HPMI that are not quite so performance critical, such as the reformatting of the matrices. It calls pcrit.s to do the most important bits.
slab.c does the work of multiply, echelize and transpose on Dfmt matrices using the best technology available. Hence it will just use Dfmt and field.c if that is the best available, which is the case except for multiply at present. It is anticipated that field-extensions will go into this layer fairly soon, and it is here that the code would need to be changed if a higher performance echelize and/or transpose were implemented.
proggies.c is the code that executed JOBs under the control of the thread farm. There are currently about a dozen functions available here, and a few more are anticipated. The work is done by calling slab.
Tfarm0,1,2 is the code for handling the JOBs submitted by the main program, and it is here that the work is shared out amongst the different threads. The task of the thread farm is to execute the submitted JOBs according to their priority, but only starting a JOB when all if its input MOJs are available. It is here that the locking is handled.
(f-layer) This layer does not exist yet, but will consist of subroutines to do things to disk files. It will do these things (e.g. echelize, multiply, transpose) by submitting jobs through the thread farm.
Program-layer-3 exposes the f-layer (once it exists) to do a job in memory. Ultimately these programs will become obsolete as the layer-4 programs are written.
Program-layer-4 works by first chopping the matrices into chunks on disk, using the f-layer to perform actions on them, and then sticking the chunks of the answer back together again. Hence the limits of meataxe64 should be set by run-time and disk-space, rather than real memory as with layer 3.
Program-layer-5 is just a dream at present, but the idea is that it works by controlling slave programs on separate machines, probably using a bespoke TCP/IP interface to move the matrix (and other) data about.